## Slide 1: Coon Creek and West Fork Kickapoo Watersheds
Design Alternatives
Discussion
September 1, 2021

## Slide 2: Watersheds Background
    Watersheds Geology
          Driftless Area (unglaciated area) of western Wisconsin
          Highly fractured sandstone susceptible to internal erosion
    Coon Creek Watershed
          3 of the 14 dams failed in 2018.
    West Fork Kickapoo Watershed
          2 of the 9 dams failed in 2018.

## Slide 3: Failed Dams
    5 Failed Dams
        Dams breached along the interface between the earth-fill and highly jointed Jordan sandstone bedrock.
        Breaches extended full depth to the valley floor.
    Additional Historic Similar Failures
        Coon Creek Watershed Site 41
        West Fork Kickapoo Watershed Site 16
        Bad Axe Watershed Sites 12 and 33

## Slide 4: 18 Remaining Dams (Watersheds Combined)
          Recently inspected to assess current conditions
          Significant deficiencies were identified in most of the dams:
                Joint deterioration in the principal spillway pipes
                Corrosion of corrugated metal pipes in the foundation drains
                Uncontrolled seepage through the dam abutments
                Not in compliance with NRCS safety and performance standards
          5 high hazard dams remaining
                WFK Pilot Klinkner Dam
                CC 17 Melby Dam
                CC 25 Baltz-Amundson Dam
                CC 33 Korn Coulee Dam
                CC 41 Dahlen Dam

## Slide 5: Alternatives Analyzed
Dam Decommissioning
Dam Replacement
No Federal Action
Dam Repair
Land Use Changes
Small Dams in Upper Watershed
Floodplain Improvements

## Slide 6: Alternatives Eliminated
Dam Repair
          Not considered a structurally sound alternative due to complex geology
Land Use Changes
          Very minimal flood protection provided
Small Dams in Upper Watershed
          Very minimal flood protection provided except small storms
Floodplain Improvements
          Will not meet purpose need on their own

## Slide 7: Failed Dam Replacement Downstream
    Replace structures immediately downstream
    Estimate costs and benefits of remaining based on the failed dams’ analysis
      Coon Creek
          $58M estimated cost to replace all dams.
          Estimated 0.14 B/C ratio
      West fork kickapoo
          $53M estimated cost to replace all dams.
          Estimated 0.09 B/C ratio without Jersey Valley rec benefits
Concrete Auxiliary Spillway
Earthen Embankment
Earthen Embankment
Earthen Auxiliary
Spillway
Original Design
Replacement Design

## Slide 8
Dam Decommissioning
    Excavate notch in the dam to pass 100-yr storm
    GRADE SLOPES TO A 2:1 SLOPE
    Embankment not removed completely
    Remove riser and outlet then grout principal spillway shut
    No sediment removal included
    Coon Creek
        $10M estimated cost to replace all dams.
    West fork Kickapoo
        $12M estimated cost to replace all dams.

## Slide 9: Jersey Valley Outlier
Strong Public support to maintain recreational benefits
$19M Cost
2.9 B/C ratio
Survey showed a shortage of outdoor recreational facilities
53.5 Acre Lake
Uses:
  Hunting
  Fishing
  Kayaking
  Beach
  Swimming
  Hiking
  Birdwatching
  Bible Camp Use

## Slide 10: Public Feedback
      Comment Focuses
          Flooding
            Dams currently provide minimal flood protection
            Land and homeowners within the ‘hydraulic shadow’ of the dams cannot escape the consequences of dam failure
          Recreation
            Strong public support to replace Jersey Valley and maintain recreational benefits
          Zoning
            Downstream zoning within the former breach inundation area of the failed dams

## Slide 11: Alternatives
      Coon Creek Watershed
          No Action (Future Without Federal Investment) – NRCS would leave structures in their current condition
          Alternative 1 – NRCS would replace all 14 dams
          Alternative 2 (preferred) – NRCS would decommission all 14 dams
      West Fork Kickapoo Watershed
          No Action (Future Without Federal Investment) – NRCS would leave structures in their current condition
          Alternative 1 – NRCS would replace all 9 dams
          Alternative 2 (preferred) – NRCS would decommission all dams except Jersey Valley

## Slide 12: Purpose and Need-
    Purpose and Need
            Evaluate alternatives for three failed dams and eleven remaining dams in the Coon Creek watershed in order to meet the dam safety standards
            Action is necessary due to the failure of five dams and the likelihood of similar failures at remaining dams
            A breach would risk life and property downstream of dams
                The breach flood elevation is higher than the (100-year) regulatory flood elevation.
            The dams have completed the Federal interest and exceeded their evaluation period of 50 years.
    To satisfy the purpose and need, the selected alternative should:
            Be based on best available science and engineering;
            Be socially, environmentally, and economically defensible;
            Reduce the threat to life and property from future dam failure.